Chem Soc Rev, TMDC: Opportunities and challenges

potential of these atomically thin semiconductors:
atomically thin transistors
vertical transistors
tunable photovoltaic

approaches to syntesize these materials

mechanical exfoliation or liquid exfoliation

due to reduced dimensionality and/or quantum confinement → exhibit unique properties distinct from their 3D bult mats

crystaline structure with few surface dangling bonds

heterostructures for totally new functions , new dimension for engineering
p-n-diodes → basis many other optoelectronic functions (photodiodes, solar cells, light emitting diodes)
p-n-diodes through vertically stacking
transistors
higher device speed
low resoluion lithography enough (limited by layer thickness but not lithography)
graphene MoS2 graphene
complete control through adding top gate electrodes
graphe TMDc → memory devices
gate driven charge separation → photovoltaics

beyond electron transport these mats are excellent hosts for ion insertion and ion transport

interesting: direct BG (due to quantum confinement effect) and non-centrosymmetric lattice structure

electrons posses a pair of inequvalent valleys in the k-space → valleytronics

demonstrated:
MoS2 FET → on/off ratio up to 8 orders of magnitude (pushing the limits of Moore‘s law)

distinctino between flakes and synthetic control of 2D-TMD

few atom thuickness → incompatible with conventional lithography (damages the atomic structure)

different cut-off frequencies (graphene > MoS2), radio frequency (RF) performance ?

Gate coupling?

Attractive for flexible electronics (currently dominated by amorpous silicon)

ambipolar behaviour → doping profile → photovoltaic effect, light emitting properties

Synthesis: top down or bottom up
CVD